## Slide 1: COA Lab Project (2016-17) The LNMIIT, Jaipur
Digital Single Lens Reflex Camera (DSLR)
Ashish Karel (15UCS027)
Ayush Soral (15UCS031)
Nitin Chaudhary (15UCS088)
Pradyumn Agrawal (15UCS096)

## Slide 2: Introduction
We are building an Instruction Set Architecture for a “DSLR Camera”. We can access the images kept in gallery and delete them.
We are developing it for a 16 - bit machine.

## Slide 3: Functions
ISO :- ISO sensitivity is a measure of the camera's ability to capture light.
Aperture : - Aperture controls the brightness of the image that passes through the lens and falls on the image sensor.
Shutter Speed : - Shutter speed is a measurement of the time the shutter is open.
Manual Focus : - Manual Focus (MF) is the system that manually adjusts camera focus.
Flash : - Used in absence of light to brighten the object.
Movie Mode : - Display the image on the screen live.
Gallery : - Display the images clicked by the camera.

## Slide 4: Functions
Zoom : - Zoom in/out the image.
Click Pic : - To take a picture.
Modes : - Various modes to automatically set few settings of camera according the mode. E.g. Panorama, Landscape, etc.
Power : - Switch On/Off the camera.

## Slide 5: Memory Model
Cell Size : 16 bits
Little Endian
Aligned Memory Instructions

## Slide 6: Registers
We will be using General as well as Special Registers.
We are using 16 registers.
Special Purpose Registers :
Program Counter
Instruction Register
Flag Register

## Slide 7: Instruction Format
Zero Operand
Halt HLT
Flash FLS
ClickPic CLP
MovieMode MME
Power POW

## Slide 8: Instruction Format
Single Operand
Shutter Speed SHS
ISO ISO
Zoom ZOM
Modes MOD
Aperture APR
Self - Timer SLT
Double - Operand
Gallery GAL
Triple - Operand
Manual - Focus MFS

## Slide 9: Instruction Design I
Name Of Instruction | Binary Code (4 bit) | Operand 1 (4 bit) | Operand 2 (4 bit) | Operand 3 (4 bit)
MFS | 0000 | XXXX | YYYY | ZZZZ

## Slide 10: Instruction Design II
Name Of Instruction | Binary Code (8 bit) | Operand 1 (4 bit) | Operand 2 (4 bit)
GAL | 0001 0000 | XXXX | YYYY
MOV | 0001 0001 | XXXX | YYYY
SUB | 0001 0010 | XXXX | YYYY
ADD | 0001 0011 | XXXX | YYYY

## Slide 11: Instruction Design III
Name Of Instruction | Binary Code (12 bit) | Operand 1 (4 bit)
SHS | 0001 0100 0000 | XXXX
ISO | 0001 0100 0001 | XXXX
ZOM | 0001 0100 0010 | XXXX
MOD | 0001 0100 0011 | XXXX
APR | 0001 0100 0100 | XXXX
SLT | 0001 0100 0101 | XXXX
INC | 0001 0100 0110 | XXXX
DEC | 0001 0100 0111 | XXXX
JMP | 0001 0100 1000 | XXXX

## Slide 12: Instruction Design IV
Name Of Instruction | Binary Code (12 bit) | Operand 1 (4 bit)
JNQ | 0001 0100 1001 | XXXX
JEQ | 0001 0100 1010 | XXXX
JLT | 0001 0100 1011 | XXXX
JLE | 0001 0100 1100 | XXXX
JGT | 0001 0100 1101 | XXXX
JGE | 0001 0100 1110 | XXXX

## Slide 13: Instruction Design V
Name Of Instruction | Escape Code (12 bit) | Binary Code (4 bit)
HLT | 0001 0100 1111 | 0000
FLS | 0001 0100 1111 | 0001
CLP | 0001 0100 1111 | 0010
MME | 0001 0100 1111 | 0011
POW | 0001 0100 1111 | 0100

## Slide 14: Instruction Types
Monadic Operation
Dyadic Operation
Arithmetic
Comparison
I/O Instruction
Data Transfer
Control Transfer

## Slide 15: Data Types
Signed Integer
Floating Point

## Slide 16: Addressing Modes
Immediate Addressing
Register Addressing

## Slide 17: Flow of Control Handling
We will initially store the all the settings of the camera in the memory cells and keep them updated with each new set of instructions.
All the operations will be handled on these set of registers.
Whole data is passed indirectly between these instructions.

## Slide 18: Fetch Cycle
PCout , R=C , MARin , Read , IncPC
WMFC
MDRoutC , R=C , IRin

## Slide 19: Microroutines
Load R1, C (Immediate Value)
Immediate_Value of IRoutC , R=C, R1in , End
Add R4, R2
R4outA , R2outC , Select A , ADD , R6in
R6outC , R=C , R4in , End
Mov R1, R2
R2outC , R=C , R1in , End

## Slide 20: Microroutines
Sub R4, R2
R4outA , R2outC , Select A , SUB , R6in
R6outC , R=C , R4in , End
CMP R1, R2
R1outA , R2outC , Select A , SUB , R6in , End
JMP R2
R2outC , R=C , PCin , END

## Slide 21: Manual Focus MFS R1, R2, R3
IN, MDRoutB, R = B, R1in
IN, MDRoutB, R = B, R2in
IN, MDRoutB, R = B, R3in
MFS
END

## Slide 22: Gallery GAL @R1, R2
IN, MDRoutB, R = B, R1in
IN, MDRoutB, R = B, R2in
R1out, MARin, READ, WMFC
MDRoutB , R = B, FILEin
R2outA , ONE, Select A , SUB , R6in
VEDEL
END

## Slide 23: SHS R1
IN, MDRoutB, R = B, SPEEDin
SHUTTER
END

## Slide 24: ISO R1
IN, MDRoutB, R = B, QUALin
ISO
END

## Slide 25
THE END